## Slide 1
https://twitter.com/tanyaofmars/status/893892863485919232
LASSO
Localize, Attribute SatelliteS in Orbit
P20151
TDoA Algorithm

## Slide 2: The TDoA simulator
Agenda
1. Time Difference of Arrival (TDoA) Introduction.
2. The Satellite Problem
3. Finding the Best Solution on a Plane
4. Fitting a Line through the solution on each plane.
5. Unit Tests
6. Simulating the Inputs
7. Deriving the Uncertainty based on Simulated Inputs

## Slide 3: Purpose Of Slides
Inform reader about how the Time Difference of Arrival algorithm works.
This is not designed as presentation slides. The slides are filled with information and comments. It is meant to be read like a paper (but with lots of pictures).

## Slide 4: TDoA Basics
By Anthony Iannuzzi

## Slide 5: TDoA data is receiver locations and time differences between each receiver.
TD represents the Time Difference data. It is an upper triangular matrix. Each entry is the time difference between the receivers represented by that row and column number.
The diagonals are zero as a station compared to itself has no time difference. The lower triangle contains redundant information and is set to 0.
The receivers must all be measured in the same frame.

## Slide 6: TDoA data creates hyperbolas and hyperboloids.
In 2 Dimensions
In 3 Dimensions
where
is the distance difference
is half the distance between stations
the distances differences is calculated by
is the speed of light in .
The half distance between stations is

## Slide 7: Graphically what hyperboloid and hyperbola look like.
2
2
These Hyperbolas assume the stations are located at . This is called the Body Frame. We will now transform this hyperbola into the Fixed Frame; the frame the stations are measured in.

## Slide 8: Coordinate Transformation Introduction
=
Azimuth, Elevation Rotations
Fixed Frame
Intermediate Frame
Body Frame
A point measured in the body frame, can be converted to the fixed frame, by multiplying by the rotation matrix
The point we want to transform

## Slide 9: Calculating Azimuth and Elevation
How to calculate Azimuth, Elevation Rotations
Fixed Frame
Intermediate Frame
Body Frame
Azimuth
Elevation
If we have the point measured in the fixed frame, then we can calculate the azimuth and elevation with respect to the fixed frame.

## Slide 10: Transforming Coordinate Axes that have different origins.
Body Frame
Fixed Frame
Intermediate Frame
Rotate to the Fixed coordinate frame orientation.
Then shift coordinate frame.
Physically, each entry in the RM can be regarded as a dot product between each body and fixed frame axis:
1.
2.

## Slide 11: Transforming the Hyperbola or Hyperboloid to the Fixed Frame. Known Data.
Given Absolute Position of Stations:
x axis always points from station 1 to 2.

## Slide 12: Transforming the Hyperbola or Hyperboloid to the Fixed Frame. The new Equation
Let , then the hyperboloid becomes:
Substitute for
split amongst the terms.

## Slide 13: Hyperboloid in Fixed Frame
Let , then the hyperboloid becomes:
Substitute for
split amongst the terms.

## Slide 14: Transforming the Hyperbola or Hyperboloid to the Fixed Frame. Visualization
2
2
1
Body Frame
Fixed Frame

## Slide 15: Creating the Hyperboloids and Hyperbolas algorithm.
Inputs is TDoA Data
Receiver Locations in the Fixed Frame
Distance Difference
Algorithm:
Calculate and offset
Create Hyperboloid in Body Frame.
Transform to Fixed Frame.
Outputs:
Symbolic Equation of Hyperboloid
Yes

## Slide 16: Changing to a 1 sided Hyperbola
2 sided Hyperbola
1 sided Hyperbola (solve for )
where
is the distance difference
is half the distance between stations

## Slide 17: Choose the Hyperbola side based on the sign of the distance difference.
The sign of is wholly dictated by sign of delta.
where
is the distance difference
is half the distance between stations

## Slide 18: Solution is much less ambiguous with 1 sided Hyperbolas
But how many hyperbolas are created from number of stations?
How do we find the “best solution”?

## Slide 19: TDoA data creates hyperboloids.
Recall the TDoA Data
For , we have 3 Hyperboloids.
For , we have 6 Hyperboloids.
Number of unique Hyperboloids.
Given , we have
Only 2 of these hyperboloids are unique.
For , we have 3 unique Hyperboloids.

## Slide 20: Intersecting Hyperbolas in 2D.
Intersection is
This works for both one-sided and two-sided Hyperbolas.
For one-sided Hyperbolas, must remove fake solutions by plugging in all solutions back into and to verify they are indeed on the Hyperbola.

## Slide 21: Removing the Fake Solutions for One-sided Hyperbolas.
Intersection is
For one-sided Hyperbolas, must remove fake solutions by plugging in all solutions back into and to verify they are indeed on the Hyperbola.
Fake solutions come from squaring both sides when going to solve the one-sided equation.
Fake Solutions

## Slide 22: The one-sided method breaks down when the sign of the Time Difference is questionable.
The one-sided method requires signed time differences.
Consider the following time differences:
The sign of TD is unambiguous in case (A).
The sign of TD is ambiguous in case (B) with respect to its uncertainty value.
Time differences approach zero as the emitter goes directly in between two receivers. TD Error becomes more significant at these points and the one-sided method may begin breaking down.

## Slide 23: Intersecting 2 Hyperboloids results in a Hyperbola.
If the Hyperboloids are one-sided, the result is a one-sided Hyperbola.
Still working on whether we can mathematically derive this hyperbola.

## Slide 24: Finding Best Solution
By Anthony Iannuzzi

## Slide 25: For one-sided Hyperbolas, finding the best solution is the average of 3 points.
The blue circle is the correct answer.
The black dot in the center of the enclosed triangular shape is the “best solution”.
Three one-sided hyperbolas intersect at 3 points only.

## Slide 26: TDoA in 2D is very sensitive to errors outside its “triangle of receivers”.
The blue circle is the correct answer.
The black dot in the center of the enclosed triangular shape is the “best solution”.
TDoA error generally looks like this:
Position error is large, but the direction is still accurate.

## Slide 27: Finding the best solution for two-sided hyperbolas is significantly harder.
Two-sided hyperbolas intersect in 12 different locations.
Which cluster is the best solution?
The one with the smallest area?
Approach:
Find all clustered locations by intersecting the hyperbolas 2 at a time.

## Slide 28: Example with no error: 2 clusters are close, but they still form a triangle.
Where are equations of Hyperboloids.
1 | 7.0001 | 0.9998
 | 7.1886 | 2.3197
 | 2.4457 | 3.8727
 | 2.0964 | 5.0562
2 | 1.9290 | -5.5781
 | 7.0000 | 1.0001
 | 2.0963 | 5.0564
 | 9.3175 | 9.0656
3 | 6.9888 | 0.9970
 | 8.0753 | 1.8799
 | 0.6839 | 4.8581
 | 2.0965 | 5.0565
Numerical precision prevents the 3 points from lining up .
Intersecting 3 hyperbolas results in no solution.

## Slide 29: First sort the data with respect to x then y. Differentiate the data. Single out the data below 0.1 difference.
 | x sorted | y sorted | difference | difference
1 | 0.6839 | 4.8581 | 1.2451 | -10.4362
2 | 1.9290 | -5.5781 | 0.1673 | 10.6345
3 | 2.0963 | 5.0564 | 0.0001 | -0.0002
4 | 2.0964 | 5.0562 | 0.0001 | 0.0003
5 | 2.0965 | 5.0565 | 0.3492 | -1.1838
6 | 2.4457 | 3.8727 | 4.5431 | -2.8757
7 | 6.9888 | 0.9970 | 0.0112 | 0.0031
8 | 7.0000 | 1.0001 | 0.0001 | -0.0003
9 | 7.0001 | 0.9998 | 0.1885 | 1.3199
10 | 7.1886 | 2.3197 | 0.8866 | -0.4399
11 | 8.0753 | 1.8799 | 1.2423 | 7.1858
12 | 9.3175 | 9.0656 |  | 

## Slide 30: Decide how many solutions there are by looking for which singled out points are clustered.
Collect the indices of all singled out differences.
Take the differences of these differences.
The number of solutions is equal to the number of non-zero terms.
Index | Diff - 1 | x sorted | y sorted | difference | difference
1 |  | 0.6839 | 4.8581 | 1.2451 | -10.4362
2 |  | 1.9290 | -5.5781 | 0.1673 | 10.6345
3 | 0 | 2.0963 | 5.0564 | 0.0001 | -0.0002
4 | 2 | 2.0964 | 5.0562 | 0.0001 | 0.0003
5 |  | 2.0965 | 5.0565 | 0.3492 | -1.1838
6 |  | 2.4457 | 3.8727 | 4.5431 | -2.8757
7 | 0 | 6.9888 | 0.9970 | 0.0112 | 0.0031
8 |  | 7.0000 | 1.0001 | 0.0001 | -0.0003
9 | 0 | 7.0001 | 0.9998 | 0.1885 | 1.3199
10 |  | 7.1886 | 2.3197 | 0.8866 | -0.4399
11 |  | 8.0753 | 1.8799 | 1.2423 | 7.1858
12 |  | 9.3175 | 9.0656 |  | 

## Slide 31: The critical points to collect are the beginning, end, and all non-zero terms in Diff-1.
The number of solutions is equal to the number of non-zero terms.
The critical points identify switching between solutions.
The first critical point is always 0.
The last critical point is the number of singled out points. (4 in this ex.)
Index | Diff - 1 | x sorted | y sorted | difference | difference
1 |  | 0.6839 | 4.8581 | 1.2451 | -10.4362
2 |  | 1.9290 | -5.5781 | 0.1673 | 10.6345
3 | 0 | 2.0963 | 5.0564 | 0.0001 | -0.0002
4 | 2 | 2.0964 | 5.0562 | 0.0001 | 0.0003
5 |  | 2.0965 | 5.0565 | 0.3492 | -1.1838
6 |  | 2.4457 | 3.8727 | 4.5431 | -2.8757
7 | 0 | 6.9888 | 0.9970 | 0.0112 | 0.0031
8 |  | 7.0000 | 1.0001 | 0.0001 | -0.0003
9 | 0 | 7.0001 | 0.9998 | 0.1885 | 1.3199
10 |  | 7.1886 | 2.3197 | 0.8866 | -0.4399
11 |  | 8.0753 | 1.8799 | 1.2423 | 7.1858
12 |  | 9.3175 | 9.0656 |  | 

## Slide 32: Use critical points to identify the indices of the solution
Index | Diff - 1 | x sorted | y sorted | difference | difference
1 |  | 0.6839 | 4.8581 | 1.2451 | -10.4362
2 |  | 1.9290 | -5.5781 | 0.1673 | 10.6345
3 | 0 | 2.0963 | 5.0564 | 0.0001 | -0.0002
4 | 2 | 2.0964 | 5.0562 | 0.0001 | 0.0003
5 |  | 2.0965 | 5.0565 | 0.3492 | -1.1838
6 |  | 2.4457 | 3.8727 | 4.5431 | -2.8757
7 | 0 | 6.9888 | 0.9970 | 0.0112 | 0.0031
8 |  | 7.0000 | 1.0001 | 0.0001 | -0.0003
9 |  | 7.0001 | 0.9998 | 0.1885 | 1.3199
10 |  | 7.1886 | 2.3197 | 0.8866 | -0.4399
11 |  | 8.0753 | 1.8799 | 1.2423 | 7.1858
12 |  | 9.3175 | 9.0656 |  | 
We now iterate through critical points, collecting all data between the previous and current critical point:
For the first solution we have
For the second solution we have

## Slide 33: The last point in the cluster is the point directly above the identified ranges.
Index | Diff - 1 | x sorted | y sorted | difference | difference
1 |  | 0.6839 | 4.8581 | 1.2451 | -10.4362
2 |  | 1.9290 | -5.5781 | 0.1673 | 10.6345
3 | 0 | 2.0963 | 5.0564 | 0.0001 | -0.0002
4 | 2 | 2.0964 | 5.0562 | 0.0001 | 0.0003
5 |  | 2.0965 | 5.0565 | 0.3492 | -1.1838
6 |  | 2.4457 | 3.8727 | 4.5431 | -2.8757
7 | 0 | 6.9888 | 0.9970 | 0.0112 | 0.0031
8 |  | 7.0000 | 1.0001 | 0.0001 | -0.0003
9 |  | 7.0001 | 0.9998 | 0.1885 | 1.3199
10 |  | 7.1886 | 2.3197 | 0.8866 | -0.4399
11 |  | 8.0753 | 1.8799 | 1.2423 | 7.1858
12 |  | 9.3175 | 9.0656 |  | 
For the first solution we have
For the second solution we have
The diff function lags one element behind. We add the next consecutive element to each solution:

## Slide 34: Finally, average the solution together.
Index | Diff - 1 | x sorted | y sorted | difference | difference
1 |  | 0.6839 | 4.8581 | 1.2451 | -10.4362
2 |  | 1.9290 | -5.5781 | 0.1673 | 10.6345
3 | 0 | 2.0963 | 5.0564 | 0.0001 | -0.0002
4 | 2 | 2.0964 | 5.0562 | 0.0001 | 0.0003
5 |  | 2.0965 | 5.0565 | 0.3492 | -1.1838
6 |  | 2.4457 | 3.8727 | 4.5431 | -2.8757
7 | 0 | 6.9888 | 0.9970 | 0.0112 | 0.0031
8 |  | 7.0000 | 1.0001 | 0.0001 | -0.0003
9 |  | 7.0001 | 0.9998 | 0.1885 | 1.3199
10 |  | 7.1886 | 2.3197 | 0.8866 | -0.4399
11 |  | 8.0753 | 1.8799 | 1.2423 | 7.1858
12 |  | 9.3175 | 9.0656 |  | 

## Slide 35: Choose the “Best” Solution Flowchart

## Slide 36: Limitations to this algorithm
This algorithm works well for 2 clusters of points.
It does not work well when there are 4 clusters of points with roughly the same size:
Averaging the points makes sense for a near equilateral triangle. It might not for an isosceles triangle.

## Slide 37
You have reached the point where the slides are updated and cohesive. This document is a work-in-progress.
11/17/2019.

## Slide 38: The Satellite Problem
By Anthony Iannuzzi

## Slide 39: Solution is much less ambiguous with 1 sided Hyperbolas

## Slide 40: Different Models of the Earth
Spherical Model
Analytical (Lat,Long) -> (x,y,z)
WGS84 Model
Matlab and Orekit Built-in functions available, not sure how they compute (x,y,z)
http://support.virtual-surveyor.com/en/support/solutions/articles/1000261351-what-is-wgs84-

## Slide 41: TDoA Receivers
Genesee Community College
Brockport
RIT downtown
Bristol UofR
Wayne County
RIT
RIT Inn
Geneseo

## Slide 43: Finding the Direction
By Anthony Iannuzzi

## Slide 44: Points on Planes to a Line Fit.
Parametric Equation of a Line:
Where
starting point of line
direction vector
is number of points
for a linear line fit
Fit a line to the data points from each plane.
For each dimension, do a linear regression fit
For 4 points:

## Slide 45: Line to Azimuth and Elevation.
Parametric Equation of a Line:
Where
starting point of line
direction vector
Earth:
Intersect Line and Earth Model
  Earth is sphere.
  Constitutes our “reference frame location”
Convert Line direction vector to Azimuth and Elevation

## Slide 46: Direction from TDoA near 0 degree elevation.

## Slide 47: Direction from TDoA at 30 degree elevation.

## Slide 48: Unit Tests

## Slide 49: 3 Station TDoA Simulator High level diagram.

## Slide 50: Algorithm Inherent Error based on Crude Ground Track is

## Slide 51: Generating Inputs to the TDOA simulator
Original by Andrew DeVries
Modified by Anthony Iannuzzi

## Slide 52
timeDiff.m
getStruct.m
dist2time.m
gnd2sat.m
geo2rect.m
Inputs:
1: Array of Latitudes, Longitudes and Elevations for G ground stations
2. Array of Latitude, Longitude, Elevation and Time Sync Errors for G ground stations
3. Array of Latitudes, Longitudes and Elevations for S satellites
4. Array of Latitude, Longitude and Elevation Errors for S satellites
GND (1xG ground stations)
SAT (1xS satellites)
Fields: lat, long, elev, lat_er, long_er, elev_er, coord[1x3], coord_er[1x3], clk
[X Y Z], [Xerror Yerror Zerror]
Loop through each Ground Station Pair for every satellite
Distances between each ground station and the satellite (also input clk)
Time Differences for each pair for each satellite
Outputs:
1: Time Differences
2: Time Difference Errors

## Slide 53
A
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Clk sync [s]
C
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Clk sync [s]
D
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Clk sync [s]
B
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Clk sync [s]
S1
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
S2
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Inputs:

## Slide 54
A
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Clk sync
C
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Clk sync
D
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Clk sync
B
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Clk sync
All information captured in GND structure!

## Slide 55
S1
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
S2
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
All information captured in SAT structure!

## Slide 56
Outputs: Time Difference Matrix
S1
Time Difference [s]
A-B
A-B error
A-C
A-C error
A-D
A-D error
B-C
B-C error
B-D
B-D error
C-D
C-D error
Time Difference Error [s]
S2
A-B
A-B error
A-C
A-C error
A-D
A-D error
B-C
B-C error
B-D
B-D error
C-D
C-D error
SN
A-B
A-B error
A-C
A-C error
.
.
.
.
.
.
(G-1)-G
(G-1)-G error
…
N satellites
G Ground Stations

## Slide 57: Notes:
timeDiff can run with any size GND and SAT structures
The coordinate conversion assumes a spherical earth
Satellite position is absolute Lat and Long, not azimuth and elevation
The elevations values are in meters above sea level

## Slide 58: Changes
Geo2rect can take any type of spheroid (really geo2ecef)
measureInTopocentricFrame takes geodetic data turns into topocentric frame.
getStruct records position in ECEF and Topocentric frame

## Slide 59: Estimating the Uncertainty
By Anthony Iannuzzi

## Slide 60: The uncertainty of some output is equal to input error times the partial derivative.
For a One-at-a-Time analysis:
Given
Then,
The partial derivatives are called the sensitivities. These identify which variables the output is most affected in. Larger errors in these mean larger error in the final answer.

## Slide 61: For complicated functions, the partial derivatives can be estimated.
For a One-at-a-Time analysis:
Given
Then,
By perturbating around the nominal inputs, we can find each partial derivative term.
Limitation: the estimated partial derivatives only apply AT those nominal conditions.

## Slide 62: For the satellite problem, the nominal input that changes is the time differences.
The driver of the time differences is the satellite location in the sky.
Receivers have error associated with them, but there nominal values never change.
The Time Differences change depending on the satellite actual azimuth, elevation, and range.
  We will estimate sensitivities for a “net” of the horizon.
https://www.chegg.com/homework-help/questions-and-answers/1-celestial-sphere-northern-hemisphere-7-points-diagram-draw-label-following-seen-observer-q23980122

## Slide 63: Errors in time tend to increase cluster spacing, increasing the area of potential locations. Precision Loss
But first… How do the hyperbolas change when there are errors in the system?

## Slide 64: Errors in location shift 2 of the hyperbolas, but the cluster size is constant. Accuracy Loss.
But first… How do the hyperbolas change when there are errors in the system?

## Slide 65
You have reached the point where the slides are updated and cohesive. This document is a work-in-progress.
11/17/2019.

## Slide 66: More than 3 base stations with small errors.
Poorly Constructed problem.
Slopes of each line are too similar – near parallel.
Slight deviations result in huge errors.
 | No error | 0.001% Location Err. | 2% Time Error
Position Err. (m) | 625 | 256,000 | 16,000

## Slide 67: 3 Base Stations with small errors.
Satellite is over Sentinel still. Stations are located on Ellingson, The Hill, and RIT Inn.
Time error is 300 picoseconds
Receiver | Error (rad)
A | 
B | 
C | 
Receiver | Error (rad)
A | 
B | 
C | 
Resulting Errors from Time Sync. One at a Time.

## Slide 68: 3 Base Stations with small errors.
Location error is Lat: 0.00005 deg, Long: 0.0001 deg, Altitude: 0.9m
Receiver | From X (rad) | From Y (rad) | From Z (rad)
A |  |  | 
B |  |  | 
C |  |  | 
Receiver | From X (rad) | From Y (rad) | From Z (rad)
A |  |  | 
B |  |  | 
C |  |  | 
Resulting Errors from Location Error. One at a Time.
Receiver | X (m) | Y (m) | Z (m)
A | 7.268079 | 4.798699 | 4.67656
B | 7.2629 | 4.802649 | 4.675313
C | 7.267696 | 4.801882 | 4.677395
Derived Location Error

## Slide 69
One at a time Plot

## Slide 70
One at a time Plot

## Slide 71: Derived Sensitivities
Parameter | Sensitivity (rad/m) & (rad/s)
 | 9.60E-05
 | 4.58E-04
 | 4.27E-04
 | 5.48E-05
 | 2.49E-04
 | 2.56E-04
 | 6.16E-05
 | 2.91E-04
 | 2.99E-04
 | 4.92E+05
 | 1.13E+06
 | 1.24E+06
Parameter | Sensitivity (rad/m) & (rad/s)
 | 9.60E-05
 | 4.58E-04
 | 4.27E-04
 | 5.48E-05
 | 2.49E-04
 | 2.56E-04
 | 6.16E-05
 | 2.91E-04
 | 2.99E-04
 | 4.92E+05
 | 1.13E+06
 | 1.24E+06
Using “total error”

## Slide 72: Solving with more than 3 stations
By Anthony Iannuzzi

## Slide 73: More than 3 base stations.
Create sets of 3 Hyperboloids.
Solve each of these individually
Intersect the resulting line fits via least squares.
Output: Single Point.
For 2 lines: