## Slide 1: Generating Inputs to the TDOA simulator
By Andrew DeVries
Progress Report 10/22

## Slide 2
timeDiff.m
getStruct.m
dist2time.m
gnd2sat.m
geo2rect.m
Inputs:
1: Array of Latitudes, Longitudes and Elevations for G ground stations
2. Array of Latitude, Longitude, Elevation and Time Sync Errors for G ground stations
3. Array of Latitudes, Longitudes and Elevations for S satellites
4. Array of Latitude, Longitude and Elevation Errors for S satellites
GND (1xG ground stations)
SAT (1xS satellites)
Fields: lat, long, elev, lat_er, long_er, elev_er, coord[1x3], coord_er[1x3], clk
[X Y Z], [Xerror Yerror Zerror]
Loop through each Ground Station Pair for every satellite
Distances between each ground station and the satellite (also input clk)
Time Differences for each pair for each satellite
Outputs:
1: Time Differences
2: Time Difference Errors

## Slide 3
A
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Clk sync [s]
C
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Clk sync [s]
D
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Clk sync [s]
B
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Clk sync [s]
S1
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
S2
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Inputs:

## Slide 4
A
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Clk sync
C
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Clk sync
D
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Clk sync
B
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
Clk sync
All information captured in GND structure!

## Slide 5
S1
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
S2
Lat, Lat error [deg]
Long, Long error [deg]
Elev, Elev error [m]
All information captured in SAT structure!

## Slide 6
Outputs: Time Difference Matrix
S1
Time Difference [s]
A-B
A-B error
A-C
A-C error
A-D
A-D error
B-C
B-C error
B-D
B-D error
C-D
C-D error
Time Difference Error [s]
S2
A-B
A-B error
A-C
A-C error
A-D
A-D error
B-C
B-C error
B-D
B-D error
C-D
C-D error
SN
A-B
A-B error
A-C
A-C error
.
.
.
.
.
.
(G-1)-G
(G-1)-G error
…
N satellites
G Ground Stations

## Slide 7: Notes:
timeDiff can run with any size GND and SAT structures
The coordinate conversion assumes a spherical earth
Satellite position is absolute Lat and Long, not azimuth and elevation
The elevations values are in meters above sea level

## Slide 8: The TDoA simulator
By Anthony Iannuzzi
Progress Report 10/22

## Slide 9: TDoA Simulator High level diagram. I/O
Inputs:
Receiver Locations:
  coordinates all measured in common frame.
  Call this the “fixed frame”
Distance Differences:
  Upper triangular matrix with 0’s on diagonal documenting every possible time difference
  Corresponds to differences.
Outputs:
Possible Locations:
  coordinates all measured in fixed frame.

## Slide 10: TDoA Simulator High level diagram. Algorithm
Create K hyperboloids in the fixed frame based on every distance difference given.
Get the intersection.
  Make a xy offset plane slice of all hyperboloids.
  Intersect the resulting hyperbolas 2 at a time.
Chose only nearby points from list of intersections. Those are the possible locations.

## Slide 11: Step 1. Creating Hyperboloids
Inputs:
Receiver Locations in the fixed frame
Distance Difference
Algorithm:
Calculate Coordinate Transformation
Create Hyperboloid in Body Frame.
Transform to Fixed frame.
Outputs:
Symbolic Equation of Hyperboloid

## Slide 12: Coordinate Transformation
=
Azimuth, Elevation Rotations
Fixed Frame
Intermediate Frame
Body Frame

## Slide 13: Coordinate Transformation
=
How to calculate Azimuth, Elevation Rotations
Fixed Frame
Intermediate Frame
Body Frame

## Slide 14: Coordinate Transformation
Offset and Rotation
Body Frame
Fixed Frame
Intermediate Frame
Rotate to the Fixed coordinate frame.
Then shift coordinate frame.
Physically, each entry in the RM can be regarded as a dot product between each body and fixed frame axis:

## Slide 15: Hyperboloid in Body Frame
where
is the distance difference
is half the distance between stations
2

## Slide 16: Hyperboloid in Fixed Frame
Absolute Position of Stations:
x axis always points from station 1 to 2.

## Slide 17: Hyperboloid in Fixed Frame
2
Let
Substitute
Result is Equation of Hyperboloid in
fixed frame.

## Slide 18: Creating Hyperboloids Recap
Inputs:
Receiver Locations in the fixed frame
Distance Difference
Algorithm:
Calculate and
Create Hyperboloid in Body Frame.
Transform to Fixed frame.
Outputs:
Symbolic Equation of Hyperboloid

## Slide 19: Step 2. Intersection
Create K hyperboloids in the fixed frame based on every distance difference given.
Get the intersection.
  Make a xy offset plane slice of all hyperboloids.
  Intersect the resulting hyperbolas 2 at a time.
Chose only nearby points from list of intersections. Those are the possible locations.

## Slide 20: Intersecting 2 Surfaces 2D
Where are equations of Hyperboloids.
Result is 2 points.

## Slide 21: Intersecting 2 Surfaces 3D
Where are equations of Hyperboloids.
Result is and

## Slide 22: Approximating 3D Intersection
Where are equations of Hyperboloids.
Solve multiple ‘planes’ of the solution.
Approximately Linear Region
Further from foci, the hyperboloids look more like planes.

## Slide 23: Step 3. Choose the “Best” Solution
Create K hyperboloids in the fixed frame based on every distance difference given.
Get the intersection.
  Make a xy offset plane slice of all hyperboloids.
  Intersect the resulting hyperbolas 2 at a time.
Chose only nearby points from list of intersections. Those are the possible locations.

## Slide 24: Intersecting 3 hyperbolas 3 times
Where are equations of Hyperboloids.
Result is 2 points.
1 | 7.0001 | 0.9998
 | 7.1886 | 2.3197
 | 2.4457 | 3.8727
 | 2.0964 | 5.0562
2 | 1.9290 | -5.5781
 | 7.0000 | 1.0001
 | 2.0963 | 5.0564
 | 9.3175 | 9.0656
3 | 6.9888 | 0.9970
 | 8.0753 | 1.8799
 | 0.6839 | 4.8581
 | 2.0965 | 5.0565
Numerical precision prevents the 3 points from lining up .
Intersecting 3 results in no solution.

## Slide 25: Getting the ‘Best’ estimate
What differences are below the specified threshold?
In this case
 | x sorted | y sorted | difference | difference
1 | 0.6839 | 4.8581 | 1.2451 | -10.4362
2 | 1.9290 | -5.5781 | 0.1673 | 10.6345
3 | 2.0963 | 5.0564 | 0.0001 | -0.0002
4 | 2.0964 | 5.0562 | 0.0001 | 0.0003
5 | 2.0965 | 5.0565 | 0.3492 | -1.1838
6 | 2.4457 | 3.8727 | 4.5431 | -2.8757
7 | 6.9888 | 0.9970 | 0.0112 | 0.0031
8 | 7.0000 | 1.0001 | 0.0001 | -0.0003
9 | 7.0001 | 0.9998 | 0.1885 | 1.3199
10 | 7.1886 | 2.3197 | 0.8866 | -0.4399
11 | 8.0753 | 1.8799 | 1.2423 | 7.1858
12 | 9.3175 | 9.0656 |  | 

## Slide 26: Getting the ‘Best’ estimate
Identify the splits between the solutions: Look for non-zero terms.
In this case, 2 solutions exist, 1 non-zero term.
Split located at non-zero terms, position two. We want to identify beginning (0) and end (4) as well.
Index | Diff - 1 | x sorted | y sorted | difference | difference
1 |  | 0.6839 | 4.8581 | 1.2451 | -10.4362
2 |  | 1.9290 | -5.5781 | 0.1673 | 10.6345
3 | 0 | 2.0963 | 5.0564 | 0.0001 | -0.0002
4 | 2 | 2.0964 | 5.0562 | 0.0001 | 0.0003
5 |  | 2.0965 | 5.0565 | 0.3492 | -1.1838
6 |  | 2.4457 | 3.8727 | 4.5431 | -2.8757
7 | 0 | 6.9888 | 0.9970 | 0.0112 | 0.0031
8 |  | 7.0000 | 1.0001 | 0.0001 | -0.0003
9 | 0 | 7.0001 | 0.9998 | 0.1885 | 1.3199
10 |  | 7.1886 | 2.3197 | 0.8866 | -0.4399
11 |  | 8.0753 | 1.8799 | 1.2423 | 7.1858
12 |  | 9.3175 | 9.0656 |  | 

## Slide 27: Getting the ‘Best’ estimate
Index | Diff - 1 | x sorted | y sorted | difference | difference
1 |  | 0.6839 | 4.8581 | 1.2451 | -10.4362
2 |  | 1.9290 | -5.5781 | 0.1673 | 10.6345
3 | 0 | 2.0963 | 5.0564 | 0.0001 | -0.0002
4 | 2 | 2.0964 | 5.0562 | 0.0001 | 0.0003
5 |  | 2.0965 | 5.0565 | 0.3492 | -1.1838
6 |  | 2.4457 | 3.8727 | 4.5431 | -2.8757
7 | 0 | 6.9888 | 0.9970 | 0.0112 | 0.0031
8 |  | 7.0000 | 1.0001 | 0.0001 | -0.0003
9 |  | 7.0001 | 0.9998 | 0.1885 | 1.3199
10 |  | 7.1886 | 2.3197 | 0.8866 | -0.4399
11 |  | 8.0753 | 1.8799 | 1.2423 | 7.1858
12 |  | 9.3175 | 9.0656 |  | 
We now do
Where is the current solution
For the first solution we have
For the second solution we have

## Slide 28: Getting the ‘Best’ estimate
Index | Diff - 1 | x sorted | y sorted | difference | difference
1 |  | 0.6839 | 4.8581 | 1.2451 | -10.4362
2 |  | 1.9290 | -5.5781 | 0.1673 | 10.6345
3 | 0 | 2.0963 | 5.0564 | 0.0001 | -0.0002
4 | 2 | 2.0964 | 5.0562 | 0.0001 | 0.0003
5 |  | 2.0965 | 5.0565 | 0.3492 | -1.1838
6 |  | 2.4457 | 3.8727 | 4.5431 | -2.8757
7 | 0 | 6.9888 | 0.9970 | 0.0112 | 0.0031
8 |  | 7.0000 | 1.0001 | 0.0001 | -0.0003
9 |  | 7.0001 | 0.9998 | 0.1885 | 1.3199
10 |  | 7.1886 | 2.3197 | 0.8866 | -0.4399
11 |  | 8.0753 | 1.8799 | 1.2423 | 7.1858
12 |  | 9.3175 | 9.0656 |  | 
Where is the current solution
For the first solution we have
For the second solution we have
The diff function lags one element behind. We add the next consecutive element to each solution:

## Slide 29: Getting the ‘Best’ estimate
Index | Diff - 1 | x sorted | y sorted | difference | difference
1 |  | 0.6839 | 4.8581 | 1.2451 | -10.4362
2 |  | 1.9290 | -5.5781 | 0.1673 | 10.6345
3 | 0 | 2.0963 | 5.0564 | 0.0001 | -0.0002
4 | 2 | 2.0964 | 5.0562 | 0.0001 | 0.0003
5 |  | 2.0965 | 5.0565 | 0.3492 | -1.1838
6 |  | 2.4457 | 3.8727 | 4.5431 | -2.8757
7 | 0 | 6.9888 | 0.9970 | 0.0112 | 0.0031
8 |  | 7.0000 | 1.0001 | 0.0001 | -0.0003
9 |  | 7.0001 | 0.9998 | 0.1885 | 1.3199
10 |  | 7.1886 | 2.3197 | 0.8866 | -0.4399
11 |  | 8.0753 | 1.8799 | 1.2423 | 7.1858
12 |  | 9.3175 | 9.0656 |  | 
Now average the solution together.

## Slide 30: Choose the “Best” Solution Flowchart

## Slide 31: Points on Planes to a Line Fit.
Parametric Equation of a Line:
Where
starting point of line
direction vector
is number of points
for a linear line fit
Fit a line to the data points from each plane.
For each dimension, do a linear regression fit
For 4 points:

## Slide 32: Line to Azimuth and Elevation.
Parametric Equation of a Line:
Where
starting point of line
direction vector
Earth:
Intersect Line and Earth Model
  Earth is sphere.
  Constitutes our “reference frame location”
Convert Line direction vector to Azimuth and Elevation

## Slide 33: Real Example with Satellite
Satellite located above the Sentinel Statue with altitude 775km
3 Stations located at the Hill, Ellingson, and RIT Inn.
Results:
Line Fit via 3 points.
 | Azimuth | Elevation
Extra | -77.76 | 43.22793
Real | -77.5685 | 42.90641
Difference | 0.1914 | -0.3215
Extra | -77.76 | 43.22793
Real | -77.5685 | 42.90641
Difference | 0.1914 | -0.3215

## Slide 34: Real Example with Satellite
Matlab appears to have a hard time creating a mesh with these large of numbers.

## Slide 35: Real Example with Satellite
Hyperboloids look like planes out this far.

## Slide 36: More than 3 base stations.
Create sets of 3 Hyperboloids.
Solve each of these individually
Intersect the resulting line fits via least squares.
Output: Single Point.
For 2 lines:

## Slide 37: Preliminary Sensitivity Analysis
Progress Report 10/29

## Slide 38: More than 3 base stations with small errors.
Poorly Constructed problem.
Slopes of each line are too similar – near parallel.
Slight deviations result in huge errors.
 | No error | 0.001% Location Err. | 2% Time Error
Position Err. (m) | 625 | 256,000 | 16,000

## Slide 39: 3 Base Stations with small errors.
Satellite is over Sentinel still. Stations are located on Ellingson, The Hill, and RIT Inn.
Time error is 300 picoseconds
Receiver | Error (rad)
A | 
B | 
C | 
Receiver | Error (rad)
A | 
B | 
C | 
Resulting Errors from Time Sync. One at a Time.

## Slide 40: 3 Base Stations with small errors.
Location error is Lat: 0.00005 deg, Long: 0.0001 deg, Altitude: 0.9m
Receiver | From X (rad) | From Y (rad) | From Z (rad)
A |  |  | 
B |  |  | 
C |  |  | 
Receiver | From X (rad) | From Y (rad) | From Z (rad)
A |  |  | 
B |  |  | 
C |  |  | 
Resulting Errors from Location Error. One at a Time.
Receiver | X (m) | Y (m) | Z (m)
A | 7.268079 | 4.798699 | 4.67656
B | 7.2629 | 4.802649 | 4.675313
C | 7.267696 | 4.801882 | 4.677395
Derived Location Error

## Slide 41
Clock A Error. Press, Pull

## Slide 42
Clock A Error. Press, Pull

## Slide 43
Clock A Error. Press, Pull

## Slide 44
Clock B & C Error. Press, Pull

## Slide 45
Clock B & C Error. Press, Pull

## Slide 46
Location Error in A. Static Shift

## Slide 47
Location Error in A. Static Shift

## Slide 48
One at a time Plot

## Slide 49: Derived Sensitivities
Parameter | Sensitivity (rad/m) & (rad/s)
 | 9.60E-05
 | 4.58E-04
 | 4.27E-04
 | 5.48E-05
 | 2.49E-04
 | 2.56E-04
 | 6.16E-05
 | 2.91E-04
 | 2.99E-04
 | 4.92E+05
 | 1.13E+06
 | 1.24E+06
Parameter | Sensitivity (rad/m) & (rad/s)
 | 9.60E-05
 | 4.58E-04
 | 4.27E-04
 | 5.48E-05
 | 2.49E-04
 | 2.56E-04
 | 6.16E-05
 | 2.91E-04
 | 2.99E-04
 | 4.92E+05
 | 1.13E+06
 | 1.24E+06
Using “total error”

## Slide 50: Next Steps
For Thursday:
Input a ground track into the simulator.
Estimate the sensitivities at each point in the ground track
Needed Inputs:
Ground Track from Orekit
Conservative uncertainties for Location Err. And Time Sync Error.

## Slide 51: Next Steps
Coming down the pipe:
Using 4 stations to yield an average direction.
Montecarlo. Allow all uncertainties to vary simultaneously
Updates to logic in TDoA when finding points.
Way in the future
Reexamine solving for a point via 4 stations.
Train a convolutional neural network to solve for the location of the satellite
  (my Machine Intelligence Term project)